EE2080 : Microprocessor Systems Lab
Experiment – 2

Submitted By : Chayan Deb
Roll No. : 121801012

Exercise-1: The commented code for Exercise-1 is attached below :

;	EXPERIMENT_1	;Title for the code
equate_val EQU 0xAAAAAAAA	;Define equate_val equal to 0xAAAAAAAA
AREA code_area, CODE, READONLY	;Telling uVision that this part is code region
EXPORT __main	;exporting to main
ALIGN	;To align everything automatically
ENTRY
__main	PROC	;Starting of the main function
LDR R1,const_val	;Load register r1 with the constant value 0X55555555
LDR R0,=const_val	;Load register r0 with the address of the constant value
LDR R1,[R0]	;Load the contents found in r0 into r1
LDRH R1,[R0]	;Load the contents found in r0 into r1 but only the last half word (16 bits)
LDRB R1,[R0]	;Load the contents found in r0 into r1 but only the last byte (8 bits)
LDR R0,=equate_val	;Load into r0, the value of the constant defined in the begining (0xAAAAAAAA)
LDR R1,=const_val	;Load into r1, the address of the constant_val variable stored in the memory
STR R0,[R1]	;Trying to store the contents of r0 into the memory location found inside r1
;But failing to do so due to the read only nature of the code region and the variable was declared inside the code region
MOV R2,R0	;Move the contents of r0 into r2
MOVS R2,#0	;Move and set the flags for moving 0 into the register r2
B __main	;Branch and go to the __main part again.... This creates an infinite loop
ENDP

const_val DCD 0X55555555

AREA data_area, DATA, READWRITE
END

Exercise-2: The commented code for Exercise-2 is attached below :

;Provide a title for the program mentioning its purpose
value1	EQU 50	;Define value1 as 50
value2	EQU 123	;Define value2 as 123
value3	EQU 0xFFFFFFF0	;Define value2 as 0xFFFFFFF0
AREA code_area, CODE, READONLY
EXPORT __main
ALIGN
ENTRY
__main	PROC
MOVS R0,#0	;Move the value 0 into R0
LDR R1,=value1	;Load the register R1 with value1
LDR R2,=value2	;Load the register R2 with value2
LDR R3,=value3	;Load the register R3 with value3
MSR APSR,R0	;Loading the special register APSR-Application PSR with the value stored in R0
ADDS R2,R1	;Add with set R2+R1 and store in R2
SUBS R2,R1	;Subtract with set R2-R1 and store in R2
ADDS R3,R1	;Add with set R3+R1 and store in R3
SUBS R3,R1	;Subtract with set R3-R1 and store in R3
MSR APSR,R0	;Loading the special register APSR-Application PSR with the value stored in R0
ADD R3,R1	;Add with set R3+R1 and store in R3
CMP R1,R2	;Compare R1 with R2 and set flags
CMP R2,R1	;Compare R2 with R1 and set flags
CMP R1,R1	;Compare R1 with R1 and set flags
CMP R1,#0x40	;Compare R1 with 0x40 and set flags
CMP R2,#0x40	;Compare R2 with 0x40 and set flags
CMN R1,R3	;Compare R1 with negative of R3 and set flags
CMN R1,R3	;Compare R1 with negative of R3 and set flags
here	B here	;infinite end loop
ENDP
AREA data_area, DATA, READWRITE
END

Exercise-3: The commented code for Exercise-3 is attached below :

;Provide a title for the program mentioning its purpose
AREA code_area, CODE, READONLY
EXPORT __main
ALIGN
ENTRY
__main	PROC
pos1	B pos3	;Redirecting to the memory address of pos3
pos2	B pos4	;Redirecting to the memory address of pos4
pos3	B pos2	;Redirecting to the memory address of pos2
pos4	B pos1	;Redirecting to the memory address of pos1 and this loop of redirecting will continue forever
here	B here	;infinite end loop
ENDP
END

Exercise-4: The commented code for Exercise-4 is attached below :

;Provide a title for the program mentioning its purpose
AREA code_area, CODE, READONLY
EXPORT __main
ALIGN
ENTRY
__main	PROC
rst_cnt	MOVS R0,#3	;move the value 3 into register R0
dec_cnt	SUBS R0,#1	;subtract with set flags R0 = R0 - 1
BNE dec_cnt	;if the zero flag is not set, go back to dec_cnt and do that operation again
B rst_cnt	;if the zero flag is set, go to rst_cnt and keep looping forever
here	B here	;infinite ending loop
ENDP
END

Exercise-5: The commented code for Exercise-5 is attached below :

;Provide a title for the program mentioning its purpose
AREA code_area, CODE, READONLY
EXPORT __main
ALIGN
ENTRY
__main	PROC
loop	LDR R0,=value1	;Loading R0 with the address of value1
BL change_value	;Branch to change_value with link to the current memory address, works like a function call
LDR R0,=value2	;Loading R0 with the address of value2
BL change_value	;Branch to change_value with link to the current memory address, works like a function call
B loop

change_value	PUSH {R1,R2}	;Pushing the values of R1 and R2 in the stack memory
LDR R1,[R0]	;Loading the address of of R0 into R1
ADDS R1,#1	;Adding the value of R1 with 1 along with setting the flags
EORS R1,R0	;Bitwise Exclusive OR operation of R0 and R1, stored in R1 and setting flags
MOVS R2,#0xFF	;Moving the value 0xFF in R2
ANDS R1,R2	;Bitwise AND operation between R1 and R2, with setting flags
STR R1,[R0]	;Store the value in R1 in the address given by R0
POP {R1,R2}	;Popping values from the stack into R1 and R2
BX LR	;Return to the address stored in the link register
here	B here	;Infinite ending loop
ENDP
AREA data_area, DATA, READWRITE
value1 SPACE 4	;Storing value1 = 4 in the data memory
value2 SPACE 4	;Storing value2 = 4 in the data memory
END

Exercise-6: The commented code for Exercise-6 is attached below :

;	EXPERIMENT_6	Title for the code
n_val EQU 4	;Define equate_val equal to 0xAAAAAAAA
AREA code_area, CODE, READONLY	;Telling uVision that this part is code region
EXPORT __main	;exporting to main
ALIGN	;To align everything automatically
ENTRY
__main	PROC	;Starting of the main function
MOVS R0, #1	; result
MOVS R1, #1	; i
loop	CMP R1, #n_val	; check if i == n_val
BEQ _end	; banch to _end if i value is equal to n_val
ADDS R1, R1, #1	; incrementing i value by 1
MULS R0, R1, R0	; multiply result with incremented value of i
B loop	; go back to loop and check the branching condition
_end	B _end	; infinite end loop
ENDP
END

Exercise-7: The commented code for Exercise-7 is attached below :

;	EXPERIMENT_7	Title for the code
n_val EQU 6	; Define n value
AREA code_area, CODE, READONLY	;Telling uVision that this part is code region
EXPORT __main	;exporting to main
ALIGN	;To align everything automatically
ENTRY
__main	PROC	;Starting of the main function
MOVS R0, #1
MOVS R1, #n_val
MOVS R2, #0
_test	CMP R0, #10
BEQ _end
ADDS R0, R0, #1
LSRS R1, R1, #1
BCS _parity
B _test
_parity	ADDS R2, R2, #1
B _test
_end	B _end
ENDP
END

Exercise-8: The commented code for Exercise-8 is attached below :

;	EXPERIMENT_8	Title for the code
AREA code_area, CODE, READONLY	;Telling uVision that this part is code region
EXPORT __main	;exporting to main
ALIGN	;To align everything automatically
ENTRY
__main	PROC	;Starting of the main function
LDR R3, _size
SUBS R3, R3, #1	;r3 having array size
MOVS R2, #0	;counter
ADR R4, _array
LDR R0, [R4]
ADDS R4, R4, #4
ADDS R2, R2, #1
_loop	CMP R2, R3
BEQ _end
LDR R5, [R4]
ADDS R4, R4, #4
ADDS R2, R2, #1
CMP R5, R0
BGT _max
B _loop
_max	MOVS R0, R5
MOVS R1, R2
B _loop
_end	B _end
ENDP

_array	DCD 1, 21, 3, -1
_size	DCD 4

END